## Slide 1
1
PRACTICAL APPROCHES FOR SOLVING LOST CIRCULATION PROBLEMS WHILE DRILLING
TEAM MEMBER
S. SAKTHI DOSS
(17612913)
M.RAJKUMAR
(17612113)
SECOND REVIEW
17/10/2020

## Slide 2
FORMULATION OF PROBLEM
INTRODUCTION
LITERATURE
REVIEW
RESEARCH
OBJECTIVES
RESEARCH
METHODOLOGY
ORGANIZATION OF
THESIS
2

## Slide 3: LITERATURE REVIEW
3
Lost Circulation Is A Broad Subject And Several Studies And Measures Have Been Introduced In The Industry To Combat It. For Example, Moore, (1986) Noted That In Shallow, Unconsolidated Formations Where The Drilling Fluid May Flow Easily Into The Formation, The Most Common Method Used To Combat Lost Circulation Is To Thicken The Mud.
He Also Stated That In Areas Such As Below Surface Casing In Normal-pressure Formations Where Natural Fractures Are Common, The Most Common Method Used To Combat Lost Circulation Is To Drill Without Fluid Returns To The Surface.
The Purpose Is To Remove The Generated Cuttings From The Hole And Deposit Them At The Lost Circulation Zone. However, This Practice Requires Large Volumes Of Water And Close Supervision As There Is The Possibility Of Encountering High Drill-string Torque And Drag.

## Slide 4
Current Research On Lost Circulation Has Been Focused On The Use Of Lost Circulation Materials (Lcms), Especially Chemical Formulations Which Have Been Proven To Be More Effective. Hamburger Et Al. (1983) Of Exxon Production Research Company Developed A Shear-thickening Fluid (STF) Which Was Tested Successfully In 10 Different Wells That Experience Severe Lost Circulation.
The Emulsion Consists Of Liquid Oil, An Oil-soluble Surfactant, And Aqueous-phase Droplets Containing Dissolved Polymer. At The Low Shear Rates Encountered While It Is Being Pumped Down The Drill Pipe, The Fluid Is A Low-viscosity, Pumpable Liquid. Yet As It Passes Through The Drill-bit Nozzles, The Resulting High Shear Rates Cause The Fluid To Thicken Irreversibly Into A High Strength Viscous Paste.
4

## Slide 5
Nayberg, (1987) Conducted Laboratory Tests That Compared The Performance Of Conventional Lcms (Granules, Flakes And Fibers) With A New High-performance Material Which Is Composed Of Thermoset Rubber In Controlling Mud Loss In Simulated Fractured Formations Using Both Water-based And Oil-based Muds. From Field Applications, He Found Out That The Use Of Thermoset Rubber Was Very Effective In Controlling Severe Mud Losses In Fractured Formations
A High Pressure Experimental Set Up Was Used To Plug Cores Of Different Permeabilities And Different Saturation Fluids. They Found Out That The Gel Formed By This Solution Could Withstand Differential Pressures Greater Than 1500 Psi Per Foot Of Plugged Formation.
5

## Slide 6
Other Researchers Have Worked On The Use Of Specially Formulated Squeeze Materials (Reactive Pills) As Lcms. Sweatman Et Al. (1997) Studied The Use Of Lost Circulation Material Squeeze Systems (LCMSS). These LCM Squeeze Systems Were Applied In Wells After Conventional Materials/Methods Failed And They Successfully Cured The Losses. Data From Field Trials Indicated That Losses Were Cured In Wells Having Temperatures Ranging From Below 80 To Over 325 Of, Highly Vugular Or Channel Zones, Weak Zones That Are Easily Fractured By Oil-based And Water-based Drilling Muds And Other Extreme Conditions. Bruton Et Al. (2001) Conducted Studies On Chemically Activated Cross-linked Pills (CACP). These Pills Are Activated By Cross-linking Agents, Time And Borehole Temperature. When Set, They Produce A Substance Described As Rubbery, Spongy, And Ductile. The Setting Time Is Fully Controllable By Using Either A Retarder Or An Activator Based Upon The Thief Formation Or Bottom Hole Temperature. However, Laboratory Tests And Field Trials Suggest That These Pills Are Not Biologically Or Chemically Degradable And Hence They Must Be Used With Caution Near Pay Zone .
6

## Slide 7: RESEARCH OBJECTIVES
The Objectives Of This Study Are As Follows:
To Review Lost Circulation Control Methods That Have Been Applied In The Drilling Industry Till Date.
To Provide The Successes And The Failures Of The Methods Presented Above In Field Applications.
To Develop Practical Guidelines That Will Serve As A Reference Material For Lost Circulation Control At The Well-site For Drilling Personnel.
7

## Slide 8: RESEARCH METHODOLOGY
The objectives of this study will be achieved through the following methods:
Read various technical journals, papers and textbooks that talk on the subject of lost circulation control over the years in the drilling industry.
Summarize these technical materials based on the various lost circulation control methods used over time, their success stories, and their failures in various field applications.
Develop practical guidelines based on the above methods.
8

## Slide 9: ORGANIZATION OF THESIS
This Thesis Is Organized Into Five Chapters.
Chapter One: Focuses On Formulation Of The Problem.
Chapter Two: Addresses The Theoretical Background To Lost Circulation Control.
Chapter Three: Focuses On The Review Of Lost Circulation Control Materials/Methods That Have Been Applied In The Drilling Industry Till Date And Their Successes And Failures In Field Applications.
Chapter Four: Involves The Development Of Practical Guidelines To Solve Lost Circulation Problems During Drilling Operations.
Chapter Five: Addresses Summary, Conclusions, And Recommendations Of The Thesis.
9

## Slide 10
THANK
YOU
10