## Slide 1
PRACTICAL APPOACHES FOR SOLVING LOST CRICULATION PROBLEMS WHILE DRILLING
UNDER THE GUIDANCE OF
Mr. VIVEK THAMIZHMANI B.E.,M.S.Petro
1
S.SAKTHI DOSS
17612913
M.RAJKUMAR
17612113
First Review
09/10/2020

## Slide 2
FORMULATION OF PROBLEM
FUNDAMENTALS OF LOST CIRCULATION CONTROL
REVIEW OF LOST CIRCULATION CONTROL METHODS
PRACTICAL GUIDELINES TO COMBAT LOST CIRCULATION WHILE DRILLING
SUMMARY, CONCLUSIONS , AND RECOMMENDATIONS
2

## Slide 3
FORMULATION OF PROBLEM
INTRODUCTION
RESEARCH OBJECTIVES
RESEARCH METHODOLOGY
LITERATURE REVIEW
ORGANIZATION OF THESIS
CONTENT
3

## Slide 4: Formulation Of Problem:
Lost Circulation Is A Common Drilling Problem Especially In Highly Permeable Formations, Depleted Reservoirs, And Fractured Or Cavernous Formations. The Range Of Lost Circulation Problems Begin In The Shallow, Unconsolidated Formations And Extend Into The Well-consolidated Formations That Are Fractured By The Hydrostatic Head Imposed By The Drilling Mud (Moore, 1986).
It Can Then Be Defined As The Reduced Or Total Absence Of Fluid Flow Up The Formation-casing Or Casing-tubing Annulus When Fluid Is Pumped Down The Drill Pipe Or Casing.
The Industry Spends Millions Of Dollars Every Year To Combat Lost Circulation And Its Associated Detrimental Effects Such As Loss Of Rig Time, Stuck Pipe, Blow-outs, And Less Frequently, The Abandonment Of Expensive Wells.
4

## Slide 5: Two Conditions Are Both Necessary For Lost Circulation To Occur Down Hole: 1) The Pressure In The Well Bore Must Exceed The Pore Pressure . 2) There Must Be A Flow Pathway For The Losses To Occur Subsurface Pathways That Cause, Or Lead To, Lost Circulation Can Be Broadly Classified As Follows.
Seepage Losses: Up To 10 Bbl/Hr Lost While Circulating. Partial Losses: 10 – 500 Bbl/Hr Lost While Circulating.
Severe Losses: More Than 500 Bbl/Hr Lost While Circulating.
Total Losses: No Fluid Comes Out Of The Annulus.
5

## Slide 6
Deepwater Drilling Has Brought Loss Circulation Control To A More Critical Level As It Involves Narrow Pore-pressure/Fracture-gradient Windows, Cold Drilling Fluid Temperatures, High Equivalent Circulating Densities (Ecds), High Cost-per-barrel Of Synthetic-based Fluids (SBM) And A High Cost For Rig Time/Non-productive Time (NPT).
6

## Slide 7
THANK YOU
7